Name: _______________________

Forces with friction

- A shopping cart mass 25 kg is pushed with a force of 110 N on a surface where (k= 0.40.

  - Draw a free-body diagram of the situation.

  - What is the normal force (Fn) the ground puts on the cart (find Fg first)?

  - What is the force of kinetic friction (Fk)?

  - What is the acceleration of the cart?

- A 179 kg piano is pushed with a force of 545 N on a surface where (k=0.25.

  - Draw a free-body diagram of the situation.

  - What is the normal force acting on the piano (find Fg first)?

  - What is the force of kinetic friction (Fk)?

  - What is the acceleration of the piano?

- A 20.0 kg box is pulled with a force of 80.0 N at a constant speed of +0.40 m/s.

  - Draw a free-body diagram of the situation.

  - What is the acceleration on the box?  What is the net force on the box?

  - What is the force of friction (Ff) acting on this box?

  - What is the coefficient of kinetic friction ((k)?

- A 95 kg crate is pushed with a force of 325 N at an angle of 25( below the horizontal.  If the coefficient of friction (() between the crate and floor is 0.20,

  - Draw a free-body diagram of the situation.

  - What are the components of the 325 N force?

  - What is the normal force on the crate (find Fg first)?

  - What is the force of kinetic friction (Fk) acting on this crate?

  - What is the acceleration of the crate?

- A 22.4 kg bag of topsoil is pulled forward with a force of 150 N at an angle of 35( above the horizontal.  If the coefficient of friction (() between the bag and floor is 0.64,

  - Draw a free-body diagram of the situation.

  - What are the components of the 150 N force?

  - What is the normal force on the bag (find Fg first)?

  - What is the force of kinetic friction (Fk) acting on this bag?

  - What is the acceleration of the bag?

- A 19 kg wagon accelerates at +1.3 m/s2 across a surface due to a 50.0 N force at an angle of 30.7( above the horizontal.

  - Draw a free body diagram of the situation.

  - Find the components of the 50.0 N force.

  - Calculate the normal force (Fn) on the wagon. (find Fg first)

  - What is the net force on the wagon?

  - What friction force is necessary for the net force to equal the answer to part d?

  - What is the coefficient of kinetic friction ((k)?